UTP, STP communication cable
Using a coaxial cable has a major drawback in the fact that the broken cable leading to the termination of the entire functionality of the network. It is entirely supplanted the use of the copper pair, which is standard in the development of this type of connection experienced a good deal of revision and is constantly evolving. Today in use for connecting wiring using cables with 4 twisted pairs (8 wires) to carry the signal. As used four pairs this means that using this type of cable can achieve full-duplex communication. The basic purpose is to connect network interface card (NIC) of the computer or other device to the network devices and interconnect network devices themselves. Basically there are two ways the performance of this cable:
- (Shielded Twisted Pair) - cable with shielded twisted-pair copper conductive netting or casing, performed with individually shielded twisted pair (STP) or with external conductive shield around all pairs (ScTP - Screened Twisted Pair). For more detailed considerations of this kind are sometimes used the name of the FTP (Foil screened Twisted Pair), when it comes to a conductive foil shielding. Armor around the plastic protective covering.
- UTP (Unshielded Twisted Pair) - cable is similar to the preceding but without conductive coating that makes it resistant to the noise and external electromagnetic influences. But modern technology overcomes this weakness. Each pair is individually wrapped and then all twisted together to resistance to external influences increase. Of course, around all pairs together is a protective plastic shield.
In both types of cable arrangement connecting the cable to the connector pair is the same. The primary difference is in the construction of cable and associated communications elements of a shielded cable with a more complex and therefore more expensive. The peculiarity of UTP is low cost and easy installation, which significantly reduces the cost of labor and additional equipment. In addition developed in particularly simple tools to connect this cable to the appropriate terminals and connectors. Connector that uses labeled RJ45 (Registered Jack - recommended plug) and is described in the ISO standard 8877. Slightly larger than a RJ11 connector which is used for the standard double-core and four-core telephone connections. This does not mean that STP cable should be avoided. On the contrary, in environments with high electromagnetic interference or when networking in older buildings, where the proximity to the source of interference can not be avoided, its use is recommended.
 Example I
Connecting unshielded UTP cable for the ISDN LAN port RJ45 plug according to 'TIA/EIA 568' standard of wiring.
xxxxxxxxxx
Sketch a picture with cable unshielded cable category 5 (five) - CAT5. It consists of four separate twisted pairs that are twisted together again. The colors are standardized. Cable category 1 (one) no twisted pairs. Other categories are in quality between these two, or better. Twisted pair cable wire resistance increases the influence of external disturbances. Way - the wiring diagram's pin RJ45 connector (pinout) with the cable is not in ascending order according to colors at image 3.6.18 drawn on the basis of 'TIA/EIA 568B Wiring' standard that is characteristic of Ethernet communication, as opposed to 'TIA/EIA 568A Wiring' standard that is characteristic of ISDN communications. When crimping the cable to the RJ45 connector, remove the shild around the pairs for about twenty millimeters, sort pairs according to standard, hard to hold the twisted pairs, align them then cut with a cutter on a tool at length of 10-12 mm, plug cable it into the connector and crimp it as shown in Figure 3.6.18e. Communication is the 'TIA/EIA 568B Wiring' standard with respect to dedicate different pairs of lines (twisted pair) cable is under the table:
PIN RJ45		ISDN	10base-T	100base-T4
1 / 2		Power 3	TxData + TxData 1+ / TxData - TxData 1-
3		TE - NT +	RxData +	RxData 2+
4		NT - TE +	Phone A	BI_Data 3+
5		NT - TE -	Phone B	BI_Data 3-
6		TE - NT -	RxData -	RxData 2-
7 / 8		Power 2	Unused	BI_Data 4+ / BI_Data 4-

Linking pair communication cable and RJ45 connectors directly connected computers (crossover) for 10Base-T and 100Base-T communication with 'TIA/EIA 568B Wiring' standard is as follows:
PIN RJ45		10base-T	10base-T (CO)	PIN RJ45 (CO)
1		TxData +	RxData +		1
2		TxData -	RxData -		2
3		RxData +	TxData +		3
4 / 5		Unused		4 / 5
6		RxData -	TxData -		6
7 / 8		Unused		7 / 8

Pairs with PINs 4-5 and 7-8 for 10Base-T and 100Base-T can be connected directly without crossing, because they are not used in the communication, which is not in accordance with T4 standard for 100Base-T4. If you can not use devices that require T4 standard will not be a problem in the communication between devices. How to identify the device used communications standard T4? Simply, one should read his instructions! Communication standard 1000Base-T uses all four cable pairs for simultaneous transmission in both directions through the use of adaptive equalization and a 5-level pulse amplitude modulation (PAM-5) technique as shown in the following table.

Linking pair communication cable and RJ45 connectors directly connected (crossover) for 100Base-T4 communication towards 'TIA/EIA 568B Wiring' standard:
PIN RJ45		100base-T4	100base-T4 (CO)	PIN RJ45 (CO)
1		TxData 1+	RxData 2+		1
2		TxData 1-	RxData 2-		2
3		RxData 2+	TxData 1+		3
4		BI_Data 3+	BI_Data 4+		4
5		BI_Data 3-	BI_Data 4-		5
6		RxData 2-	TxData 1-		6
7		BI_Data 4+	BI_Data 3+		7
8		BI_Data 4-	BI_Data 3-		8

In all cases the maximum allowable cable length is 100 m, although this distance is not recommended for the 'crossed' to do, because there is no HUM (or switch) to bring about some kind of amplification stable communication. Displayed scheme described for 10Base-T and 100Base-T, with different categories of UTP cable used to connect devices. In the first case it is a C3, C4 or C5, in the second case it is a C5 or C5E, in the third case, it is a C6. Will it be 'crossed' or not depends on which devices are connected. Simply put, the devices of different families are connected with a cable of the same orientation (straith-through) as the NIC-HUB or HUB-ROUTER, and devices of the same family are associated with the 'crossed' cable (crossover) as the two NIC or two HUB. Category cable depends on the speed of data transfer and the criteria are tightened as speed increased.

Example II
Chronological sequence and properties of certain categories of UTP cable, the approximate representation of more than 50% of new network systems (not by year of publication and the establishment of standards), would be:
Category	Year	Speed (Mbps)	Frequency (MHz)	Curlicues at 1m	Usage
C1	<1983	< 1	1	0	telephony and ISDN
C2	1983	4	10	2 - 3	telephony and ISDN
C3	1993	100	16	3 - 4	ISDN, 4 Mbps TR, 10base-T, 100base-T4
C4	1994	100	20	15 - 17	ISDN, 16 Mbps TR, 10base-T, 100base-T4
C5	1998	100	100	24 - 25	ATM, TR, 10base-T do 100base-T
C5e	1999	1000	350	24 - 25	ATM, TR, 10base-T do 1000base-T
C6	2004	10000	200 - 550	> 25*	ATM, TR, 10base-T do 10000base-T
C7	2010	10000	600 - 1000	> 25**	STP (non RJ-style) or RJ45 - 10base-T do 10Gbase-T

* Cable category C6 has a slightly convoluted plastic core, cross-section, for better separation pair, who are of course each of them curled. He acts as if the cable C5E categories connects to circuits lower categories, so backward compatibility is preserved. When crimping, this plastic guide should be cut off in the plane with a protective shield. ** Cable category C7 is a shielded cable in which some conductive foil shielded twisted pairs and entire cable conductive netting - S/STP. Each pair can be special connectors to connect in a way that benefits each pair separately (analog phone) or two wires together (Internet or VoIP) or to join the pair cable for CATV (cable TV). So, patch panel and the wall socket (outlet) is more complex compared to the RJ45 standard, but also versatile. Connectors are different in accordance with the purpose and supported by the simultaneous operation of multiple simultaneous applications through the same cable but different pair, as shown in Figure 3.6.19b.

The higher the category of copper cable the greater the demands on the resistance to interference and crosstalk between each pair. But an increasing share of the communications with optical and wireless systems. But the transmission of signals over copper lines still remains a reference for dealing with basic access to the user. It can be expected that from the standpoint of cost, installation, and security prevail use cable with copper wires.